CL7206C4 4-port Split-Type RFID Reader

Features:

- Impinj R2000 platform and double power amplifier synthetic circuit.

- Read distance up to 20 meters, read speed 400 times/sec.

- Linux OS carrying ARM9 CPU keeps 24hrs X 365days running.

- Kinds of communication interfaces. WiFi, Bluetooth optional.

Specification:

| System |
| --- |
| Operation System: | Linux 2.6 |
| CPU: | ARM9, 400MHz |
| Memory Capacity: | DDR SDRAM :128M; ROM: 256M |
| UHF RFID |
| Protocol: | ISO/IEC18000-6B, 6C / EPC C1Gen2 |
| Frequency: | USA: 902 MHz-928MHz (FCC part 15) EU: 865-868MHz (ETSI EN 302208) |
| Output Power: | 0dBm-33dBm (±1dBm) adjustable |
| Power adjustment: | 1dBm step-by-step |
| Channel bandwidth: | ＜200KHz |
| Frequency stability: | ≤±10ppm |
| Work Mode: | Fixed/hop frequency optional |
| Reading speed | >400times/S |
| Anti-collision | Support multi-tag reading, intensive reading |
| Software | Support RSSI, antenna detection, online update, data filtering |
| Read range: | 0-20m (depending on environment) |
| Write range: | 0-8m (depending on environment) |
| Antenna interface: | 4×TNC interface |
| Interface: | RS-232, RS-485, Wiegand, RJ45, USB2.0 (WiFi, Bluetooth can be added) |
| I/O interface | 4 input/ 4 relay output |
| Physical |
| Working Temperature: | -20 - +70°C |
| Storage Temperature: | -40 - +85°C |
| Atmospheric Pressure: | 86kPa～108kPa |
| Relative Humidity: | 10~9% RH no condensing |
| Size: | 256mm*148mm*43.5mm |
| Weight: | 2.0Kgs |
| Housing Material: | Casting aluminum |
| Power supply: | (60W) DC 24V/2.5A (DC 9V ~ 30V) |
| Protection level: | IP55 |